## COPING WITH MAJOR SPILLS INVOLVING GMOs

In the event of a spill, the following procedures should be observed:

- Avoid breathing in aerosol and vacate the area.

- Warn other people to keep away from the area (verbally and with signs).

- Keep the area cleared for a minimum of 30 minutes to allow time for aerosols to settle or be diluted by air handling systems.

- Remove contaminated clothing.

- Wash exposed skin.

- Notify laboratory supervisor/ facility manager.

- If there is a significant risk of infection, consider assembling a clean-up team consisting of three people: one observer and two operators.

- Use personal protective equipment for infection control (gown, gloves, goggles, respirator)

- After waiting at least half an hour and wearing protective clothing: assess the extent of the contaminated area.

- Lay paper towels impregnated with disinfectant (hypochlorite) over the spill.  Wait at least 10 minutes.

Do not pour disinfectant directly onto a spill as this can produce more aerosols.

- Wipe over the contaminated area with disinfectant.

- Transfer contaminated objects to suitable containers for disposal.

Do not steam sterilise material wetted with hypochlorite as toxic chlorine vapour will be produced.

- Decontaminate or steam sterilise protective clothing or equipment.

- Complete an ‘incident report’.

- Notify your supervisor and the Institutional Biosafety Committee.